SALES QUOTATION

Nanoparticle Size Analyzer VASCOKIN

Quote reference: 	xxxx

Date: 	xxxx

Validity:	xxxx

Contact: 	[First Name] [Nast Name]

e-mail:	xxx@yyy.com

Phone: 	+xx xxxxxx

Website: 	www.yyy.com

A l’attention de :

[First Name] [Nast Name]

Company

Adress (street, ZIP CODE, TOWN, COUNTRY)

contact@zzz.com

Madam, Sir,

As per your kind request, please find hereafter our formal quote for our new generation Particle Size Analyzer VASCO Kin equipped with a remote optical head for in situ measurements. This offer includes the basical configuration and an optional full services pack. Feel free to call us back to discuss about make this device matching your requirements and needs.

VASCO Kin

In situ PSD analyzer

Best Regards,

#1. VASCO Kin [Basic] : Particle Size Analyser with optical remote head for in situ measurements.

Particle Size Analyzer based on Time-Resolved Dynamic Light Scattering technology (TR-DLS) and UNIQUE integrated optics for remote and contactless experiments.

| SPECIFICATIONS |
| --- |
| Size Range (Hydrodynamic Diameter) | 0.5 nm à 10 µm * |
| Concentration | 1.10-5 % to 40 % weight * |
|  | *Sample dependent limits |
| DLS Core |
| Detector | APD Photon-counting Module High sensitivity, artefact-free and ultralow noise sorted detector Possibility to add a fluorescence rejection filter. |
| Laser | Laser diode@ 638nm – minimum 45mW (other contact us) Life time > 25 000 h Frequency locked – ultra low-noise for improved stability and better SNR |
| Laser Safety | Double interlock including 1 keylock Removable beam dump with holder |
| Temperature range | -10 to +110°C Solvent proof Pt100 sensor |
| Dimensions / Weight | 220 x 220 x 64 mm3 (LWD) / 2.5 kg |
| in-situ optical head |
| Principe | Remote and contactless measurement within a transparent window of the sample container: no intrusiveness, no contamination risk, no sample manipulation. Robust and compact: small form factor, no moving parts, easy to integrate in harsh environment or with restrictive access, insensitive to stray light and parasitic radiations. Integrated alignment laser beam switch for a quick and accurate placement of the remote head. Flexibility et customization : interchangeable heads – easy replacement Low usage costs: No maintenance, no consumables, no sample batching. Signal improvment : Possibility to add a fluorescence rejection filter and/or a polarizer on the detection path (contact us about this option). Ideal for contactless measurement within glass capillaries, any vials, reactors, climatic chambers, glove boxes, synthesis monitoring and feedback loop applications |
| Detection angle | 170° ( other contact us ) |
| Minimum sample volume | < 4µL | Container material dependent |
| Solvent proofness | Any solvent |  |
| Weight | < 0.4 kg |
| Dimensions | 50 x 25 x 120 mm3 (LWD) – Umbilical cable: 2m std. ( other contact us ) |
| Accessory | Versatile Mechanical holder for in-situ head Reproductible placement of the sample vial Laser safety beam dump Simple Alignment (rail translation stage with blocking screw) 3D printed vial support (3 models are supplied) (Drawing files provided on demand for free) |
| COMPUTER AND nano Kin SOFTWARE |
| PC | Supplied with dedicated embedded PC - avec ordinateur PC nano Kin™ software priorly installed. Computer Base (220x220x48 mm3) + 17’’ Monitor |
| Licenses | Unlimited users license issues. One license per Computer. Activation softkeys provided within 24h. |
| Updates | Free, without limit in time Hard-copy (CD-ROM, USB stick) or downloadable from the web. Backward compatibility assured except for major updates. Updated Users manual |
| Main features of nano Kin™ software | Log in profiles: Administrator, Expert, Operator Running Modes: Measurement, Simulation, Post-analysis (import) Intuitive navigation (sequential) Time slicing and kinetics mode: UNIQUE technology allowing to monitor fast kinetics and/or accurate reproducibility measurements (time resolution as low as 200ms). Readable data and plots : Data/plots export on the fly (right click to clipboard) Report file format : .pdf or .rtf (writer software compliant) Inverting Algorithms : CUMULANTS : monomodal sample with monodispersed trend PADE-LAPLACE (proprietary) : Discrete mathematical method for polymodal sample. No griding. SPARSE BAYESIAN LEARNING (SBL ; proprietary ) : Continuous distribution mathematical method for polymodal sample. No a priori is required about the expected distribution slope. Probabilistic calculation module with self-learning method applied on the regularization parameter. Optimized L-curve representation to suggest the best solution. Grid = 250 classes, Log scal : 0.1nm to 10µm. |
| Compliancy and certifications |
| International Standard | DLS measurement: ISO13321 & ISO22412 Equipment : EN-613226/A1 & EN-61010-1 (CEM et Electrique) EN-60825-1 (Laser Safety) CE Compliancy: Vasco Kin™ is a certified product According to 2006/95/EC & 2004/108/EC directives |
| VASCO Kin™ is a scientific instrument fully imagined, designed and manufactured by Cordouan Technologies in our French HQ (Pessac, FR) |
| After-sales Support |
| Installation & Training | Within 2 weeks after delivery, on site installation and training for users (provided by a qualified engineer) (no limitation on the number of participants, minimum half-day according to the DLS skills of the audience – Date to be defined after delivery) Reminder on Light Scattering theory (Static and dynamic) ; Cordouan’s product unicity : DTC, Autocorrelation, Highly resolved measurement, Time-slicing, Results analysis and interpretation (algorithms Fits and residuals), aggregation behaviors. Getting started with Nano Kin Software: Installation on a PC - Users accounts management – S.O.P (Standard Operating Procedures) – Advanced parameters - measurements - Report editing – Excel export; Practical case: measurement of customer representative samples. |
| Warranty and Support | Nominal term of warranty : 1 year Parts & Labor In case of problem, contact e-mail adress : service@cordouan-tech.com A first diagnosis will be performed through internet connexion (if permitted). If the issue is hardware, it will be agreed on a case by case basis: Either a visit on the customer site under 15 days. Or a back shipment of the unit to our HQ (transport expense is Cordouan’s charge) Cordouan has been committed since its incorporation to guarantee to its customers a maintenance and repair time of less than 15 days (including transport). |
| Unit Price for set #1 (ex-VAT): | 53 700 € |

#2. Services & Maintenance Pack (Premium)

This offer includes the whole compliancy and after-sales support options.

| Compliancy and certifications |
| --- |
| Traceability et GMP (Good Manufacturing Practice) | Compliancy: 21 CFR Part 11 (US FDA) – software extension + IT administrators training + documents IQ/OQ Management – training and on-site certification (½ day) |
| Control sample kit | NIST Certified sample kit (with certificat) – Polystyrene spheres. PSL 100 nm 15 mL cc. 1%wt PSL 30 nm 15 mL cc. 1%wt |
| After-sales Support |
| Installation & Training | Direct hot-line with the trainer for 1 year. (help for results interpretations, additional information, advices for sample preparation protocols) |
| Scientific Support | Support from our application lab for methods and protocols validation. |
| Maintenance | 1 maintenance visit for the duration of the warranty period. (To be scheduled at least 30 days before) |
| Warranty and Support | +1 year Total term of warranty : 2 years Parts, Labor and on-site intervention In case of Problem: immediate assistance working days (09h-18h GMT+1): Hotline number (+33).xx / service@cordouan-tech.com If the issue is hardware, it will be agreed on a case by case basis: Either a visit on the customer site under 5 days. Or free of charge replacement of the failed unit with an equivalent one under 72h |
| Unit Price for set #1 (ex-VAT): | 9.200 € |

Summary – Quote xxxxx/Vasco Kin

| Item | Description | Qty | Unit Price ex-VAT HT |
| --- | --- | --- | --- |
| #1 | Vasco Kin [Basic] – particles size analyzer Set including: 1 DLS Core unit + 1 in-situ head 1 Mechanical holder 1 priorly configurated PC base + Monitor nano kin software w/o license limit. Free Upgrades On-site installation and training 1 year of support and warranty | 1 | 53.700 € |
| #2 | Pack Service & Maintenance (Premium) Set including: GMP : 21-CFR chapter 11 module + IQ/OQ Management NIST-certified control kit 1-year direct Support from trainer Application lab Support on protocols 1 maintenance visit / year + 1-year extended warranty On-site repair or free of charge replacement | 1 | 9.200 € |
| PORT | Shared shipping and handling costs | 90 € |
|  | TOTAL | 62.990€ |
| OPTIONAL CUSTOMIZATION |  |
| #3 | Our Development team will be glad to help you designing mechanical parts, electronics or software applications to optimize the coupling of Vasco Kin with your setup. Feel free to contact us. |

Terms :

Currency:		Prices in Euros (€), local VAT excluded

Validity:		90 days

Incoterm:  		Ex-WORKS

Delivery:		6 to 8 weeks after Order Acknowledgement.

Term of Payment: 	30 days end of month – Invoice emitted at shipment.

Country of Origin: 	Design and Manufacturing in France.

General Selling Conditions of CORDOUAN Technologies SAS