Quote Number: 	Pcom-MBN_VASCO+WALLIS-EN-07.11.2017

Date:	07.11.2017

Quote Expires:	8 weeks

Contact: 	Sylvain Boj – Sales & Marketing

Mail:	sylvain.boj@cordouan-tech.com

Tel:	+33 (0)5 56 15 75 46

Web site: 	www.cordouan-tech.com

Attention to: XX

Dear Mr XX,

Herewith you will find the requested quotation for the CORDOUAN zeta potential measurement, Model WALLIS according to the general terms and conditions of sales by French law.

Principals Features:

- Zeta potential measurement +/- 200 mV.

- Concentration 0,0001 to 10wt%

- Control of the CORDOUAN zeta potential by software using MS-Windows, Windows 2000 or windows seven.

We are looking forward to hear from you and hope that our offer will meet your expectations. Please don’t hesitate to contact us you have any questions.

Best regards

Sylvain Boj

Sales Development Manager

Phone : +33 (0)556 158 045

Fax : +33 (0)547 747 491

E-mail: sylvain.boj@cordouan-tech.com

Poste 1/ ZETA POTENTIAL ANALYZER

| Zeta Potential | Zeta potential range | -200 mV to 200 mV (*) |
| --- | --- | --- |
|  | Mobility range | 10-11 to 10-7 m2/V.s (in water) |
|  | Particle Size range (radius) | 1 nm to > 50 µm - up to 100 µm (*) |
|  | Maximum sample concentration | 0.0001% to 10% w/% (*) |
|  | Cell options | Cuvette cell with optical quality windows for aqueous and organic solvents |
|  | Sample volume | Typically 750 µL (Hellma cell – 10 mm light path) |
|  | Maximum sample conductivity | 300 mS/cm |
|  | Sample Type | Aqueous & organic solvents – pH: 1-14 (depending on cuvette cell material) |
| Signal processing | Principal technology | Laser Doppler Electrophoresis (LDE) |
|  | Standard laser | 20 mW diode pumped solid state (DPSS) single-longitudinal @635 nm coupled to automated attenuation system. Other wavelengths available upon request |
|  | Measurement angle | One angle for zeta potential at 17° |
|  | Fast Fourier transform Algorithm | 0,1 Hz resolution for Doppler frequency |
|  |  | Resolution in zeta : - 10-10 m2/V.s or 0,1 mV ( in water) |
|  | Detector | Avalanche Photodiode – APD (*) ( option of PM) |
| General | Temperature control range inside the cell | 10°C to 70°C +/-0,1°C - option to 90°C available |
|  | Computer interface | USB 2.0 – Windows XP, Seven |
|  | Dimensions | 45 cm x 30 cm x 40 cm (HWD) |
|  | Weight | 17 kg |
|  | Power | 100/115/220/240 VAC, 50/60 Hz, 100 W max |
| System Compliance | CE certification | CE marked product - Class I laser product, EN 60825-1:2001, CDRH |
|  | ISO norm | ISO 13099-2 : 2012 – Colloidal system – methods for zeta-potential determination – Part 2 : Optical methods |
|  |  | CFR part 11 |
| (*)Sample type dependant |  |  |

- Easy portable instrument 33 * 38.3 * 22 cm/ recommended to be used with “Pelicase” transport case with rollers (see option).

F.C.A Net Price : 25.000,00 €

Prices 				In Euros €, Total price F.C.A. Bordeaux Airport France

Terms	30 days after receiving the invoice

Bank Details 		On demand after order acknowledgement.

Delivery Time 	4-8 weeks in standards following payment term. Need to be confirm A.R.O

Validity 		90 days

Country of Origin		Europe

Warranty 	- 12 months in standards except all consumables parts: O’rings, tube for on-line option, samples for calibration (depend of stock condition).

- Add 5% at the final configuration for extended of additional years.

- Spares and labor based on return of the instrument at CORDOUAN factory at user’s cost.

Price 				Net Price.